## Slide 1: Wireless Design for Voice
Last Update 2011.06.11
1.0.0

## Slide 2: VoWLAN QoS
Note that a VoWLAN phone is expected to have the same QoS of a desk phone, not like a cell phone
We all expect dropped calls when using cell phones, but that will not be accepted at all for VoWLAN
As VoWLAN users roam throughout the enterprise or a “hot zone,” their calls will be handed off to multiple APs

## Slide 3: VoWLAN QoS
If these APs belong to the same IP subnet, this handoff is performed at Layer 2; if the move is across subnets, the handoff is at Layer 3
Roaming between APs inevitably involves some delay or latency

## Slide 4: VoWLAN QoS
In a voice call, this latency should be less than 50 milliseconds; otherwise, the connection will be dropped or the call quality will severely degrade
Layer 2 roaming latency is mainly due to three processes: scanning, reassociation, and reauthentication

## Slide 5: VoWLAN QoS
Using current standards-based mechanisms (active scanning, 802.11F Inter-Access Point Protocol, and 802.1x authentication), handoff latency can vary from a few hundred milliseconds up to several seconds, clearly unacceptable for voice

## Slide 6: VoWLAN QoS
The most time-consuming process is 802.1x, which requires the mobile device to be reauthenticated with the RADIUS server every time a call is handed off between APs
This can take a few seconds

## Slide 7: VoWLAN QoS
In order to reduce latency to acceptable levels, vendors of centrally controlled WLANs have implemented several proprietary mechanisms
Some of these employ “pre-authentication” techniques, in which the controller distributes security/keying information, the cached Pairwise Master Key (PMK), to neighboring APs

## Slide 8: VoWLAN QoS
Other schemes tunnel all 802.1x authentication (and all other) traffic from the APs up to the controller or switch so it can centrally and rapidly manage the mobility between APs
With Layer 3 roaming, the mobile device must request and obtain a new IP address from a DHCP server, which again take several seconds

## Slide 9: VoWLAN QoS
In order to avoid that delay, centralized architectures
use various proprietary Mobile IP or Proxy ARP/IP tunneling techniques that enable the client to keep existing sessions and connectivity on the new subnet without having to actually change its IP address

## Slide 10: VoWLAN QoS
The IEEE is working on several emerging 802.11-based standards that will help achieve fast secure roaming
The main one is 802.11r (Fast Roaming/BSS Transition)

## Slide 11: VoWLAN QoS
It will be supplemented by 802.11i for pre-authentication and 802.11k (Radio Resource Management), which will enable the handset to make fast roaming decisions by prediscovering neighboring APs; their distances; and call capacities

## Slide 12: VoWLAN QoS
Until these standards-based solutions are ratified and implemented in commercial products (not before end of 2007 or beginning of 2008), proprietary centrally controlled schemes will remain the only option

## Slide 13: VoWLAN Mobility
Wired VoIP deployments have made it clear that call quality depends chiefly on the voice codecs used (such as G.711, G.729, or iLBC) and on end-to-end latency, jitter (variations in delay), and packet loss
VoWLANs are subject to the same end-to-end parameters

## Slide 14: VoWLAN Mobility
The main differences are that a WLAN relies on a shared airlink; uses different access mechanisms than wired Ethernet (CSMA/CA 802.11 vs. CSMA/CD 802.3), exhibits relatively limited bandwidth, and features higher packet-error rates and packet overhead

## Slide 15: VoWLAN Mobility
WLAN QoS mechanisms are critical when voice and data share the same RF band. Data traffic typically consists of bursty transmissions and various-sized packets
Some of these can be very large (file downloads, for instance) and take more time to transmit over the airlink

## Slide 16: VoWLAN Mobility
This delays smaller, continuously transmitted voice packets, since all traffic contends for the shared medium using collision avoidance, and increases both latency and jitter
QoS mechanisms rectify this situation by prioritizing voice over other traffic (data and video) and by providing voice with faster, more timely access to the medium

## Slide 17: VoWLAN Mobility
Until recently there were no WLAN QoS standards, prompting some vendors to develop proprietary protocols
The most notable and widely deployed of these is SpectraLink Voice Priority (SVP), which has become a de facto standard and is supported by most WLAN infrastructure vendors

## Slide 18: VoWLAN Mobility
SVP basically violates the 802.11 media access control (MAC) standard by assigning voice packets a back-off value of zero, which gives them absolute priority over other traffic. The downside is that if there are many wireless VoIP phones active on a single AP, there will be too many collisions

## Slide 19: VoWLAN Mobility
Moreover, the phones can monopolize available bandwidth and starve conventional data transmissions

## Slide 20: VoWLAN
Alcatel-Lucent goes on some more, but you get the idea